## Slide 1
Control of linear vibrations
Alberto Ficicchia, Alessio Russo, Gianluca Savaia
School of Industrial and Information Engineering
Politecnico di Milano
AUTOMATION AND CONTROL LABORATORY
Automation and Control Engineering 2015/2016
https://github.com/rssalessio/linearVibrationsControl

## Slide 2: System description Control of linear vibrations
POLITECNICO DI MILANO
Brushed motor
Incremental encoder
Cart
Weight
Arduino board
Spring
Automation and Control Laboratory – Ficicchia Russo Savaia
Notes: Fare due slide e più figure e meno testo

## Slide 3: Preliminary issues Control of linear vibrations
POLITECNICO DI MILANO
Measurement saturation
Solved
Measurement noise
White noise
+ det. comp.
Variable variance
Solved
Solved
Fourier analysis
LS estimation
Automation and Control Laboratory – Ficicchia Russo Savaia
Notes: Fare due slide e più figure e meno testo

## Slide 4: Protection system: four macroblocks Control of linear vibrations
POLITECNICO DI MILANO
Input manager:
Selects input, applies noise
Protector (state machines):
Saturates voltage, displacement and reference
Synchronizes Arduino and signal starting time
Triggers alert
System:
Motor and encoder feedback
Controller:
Contains control action
Automation and Control Laboratory – Ficicchia Russo Savaia
Notes: Fare due slide e più figure e meno testo

## Slide 5: Modelling Control of linear vibrations
POLITECNICO DI MILANO
Modelling
Automation and Control Laboratory – Ficicchia Russo Savaia
Notes: Fare due slide e più figure e meno testo

## Slide 6: Modelling: motor Control of linear vibrations
POLITECNICO DI MILANO
where
: back-emf effect
: torque constant
: motor torque
Linear first order system:
Automation and Control Laboratory – Ficicchia Russo Savaia
Notes: Mettere foto carrellino
Fare sezioni a scomparsa con immagini riferite al pezzo del modello

## Slide 7: Modelling: pinion/rack Control of linear vibrations
POLITECNICO DI MILANO
: load torque transmitted to the carts
: inertia of motor, pinion and rack
: non linear motor friction
Pinion/rack:
where:
Automation and Control Laboratory – Ficicchia Russo Savaia
Notes: Mettere foto carrellino
Fare sezioni a scomparsa con immagini riferite al pezzo del modello

## Slide 8: Modelling: carts Control of linear vibrations
POLITECNICO DI MILANO
: total damping (viscous + spring) of the i-th cart
Setting and neglecting nonlinear friction
where
Each cart: where
Automation and Control Laboratory – Ficicchia Russo Savaia
Notes: Mettere foto carrellino
Fare sezioni a scomparsa con immagini riferite al pezzo del modello

## Slide 9: Equations: 1-2-3 DOF Control of linear vibrations
POLITECNICO DI MILANO
2-3 DOF: Lagrangian approach: where
1 DOF
2 DOF
3 DOF
Automation and Control Laboratory – Ficicchia Russo Savaia

## Slide 10: Identification Control of linear vibrations
POLITECNICO DI MILANO
Identification
Automation and Control Laboratory – Ficicchia Russo Savaia
Notes: Fare due slide e più figure e meno testo

## Slide 11: White box identification: steps Control of linear vibrations
POLITECNICO DI MILANO
1. Define a model for the system
2. Perform a set of tests on the real system
and collect the relevant data
3. Use model to get the wanted parameters from measured data
4. Perform a simulation of the system with the identified parameters
5. Validate the results comparing the simulation output with the real one
How to compare?
Which metric?
Automation and Control Laboratory – Ficicchia Russo Savaia
Notes: Voltaggio a onda quadra con corrente che lo segue e fare vedere che la disatnza a steady state è R. L’abbiamo idnetificata cosi.
Per la fuznione di straferimento mettere il blocchetto di simulink nei modelli

## Slide 12: Validation cost function Control of linear vibrations
POLITECNICO DI MILANO
Simulated output
Real output
Distance expressed by L2 norm
represents the energy of the difference signal
A more practical index is:
In this way d=1 represents a perfect fit
Automation and Control Laboratory – Ficicchia Russo Savaia
Notes: Voltaggio a onda quadra con corrente che lo segue e fare vedere che la disatnza a steady state è R. L’abbiamo idnetificata cosi.
Per la fuznione di straferimento mettere il blocchetto di simulink nei modelli

## Slide 13: Motor identification: resistance Control of linear vibrations
POLITECNICO DI MILANO
Steady state: identify
Voltage
Current
Transient
Steady state
Automation and Control Laboratory – Ficicchia Russo Savaia
Notes: Voltaggio a onda quadra con corrente che lo segue e fare vedere che la disatnza a steady state è R. L’abbiamo idnetificata cosi.
Per la fuznione di straferimento mettere il blocchetto di simulink nei modelli

## Slide 14: Motor identification: inductance Control of linear vibrations
POLITECNICO DI MILANO
Matlab tfest (first order)
Nominal values from datasheet
Validation with input
Fit = (81.42±3,64) %
From data
Automation and Control Laboratory – Ficicchia Russo Savaia
Notes: Voltaggio a onda quadra con corrente che lo segue e fare vedere che la disatnza a steady state è R. L’abbiamo idnetificata cosi.
Per la fuznione di straferimento mettere il blocchetto di simulink nei modelli

## Slide 15
Identification
Cart identification

## Slide 16
Identification
Mass of the cart?
Damping and stiffness of the springs?

## Slide 17
Identification
To find the stiffness of the spring and the mass of the cart we need two equations..
Since we have 2 unknown variables! But what coefficient do we change? The mass!
We know the load!
: natural pulsation with additional load
natural pulsation without any load
load in kilograms
mass of the cart in kilograms
stiffness of the i-eth spring
Remember,

## Slide 18
Identification
Validation
Identification: use same x(0)
Validation: random x(0)
Friction effect!
Orange: simulated signal
Blue: real signal

## Slide 19
Identification
Overall system
Identification

## Slide 20
Identification
So far we estimated the main parameters of the motor, and of the cart.
We still miss:
  Electrical torque constant
  Inertia of the motor/pinion/rack
  Induced stiffness and damping of the motor

## Slide 21
Identification
Force transmitted from the motor:
Diameter of the pinion
Electrical torque
constant
To identify gamma use:
Where infinity stands for steady state
What about electrical torque constant?
Remember,
,

## Slide 22
Identification
Validation – 1 DOF
Used white noise for validation! Friction effects are still visible
85.42% of fit

## Slide 23
Identification
Validation – 2 DOF
87.29% of fit for the first cart, 85.79% for the second one. Plots shown only for
the second cart

## Slide 24
Identification
Gray Box Identification

## Slide 25
Identification
Since the identification process was long, we first used a rapid approach to estimate
All the variables in play.
Feed a train of pulses into the system and measure both the current and
displacement of the cart
Measured
Simulated

## Slide 26
Identification
Motor
Cart
Identification results

## Slide 27
Identification
Non Linearities Identification

## Slide 28
Identification
During the course of the project we found many non-linearities, especially in the
Motor, responsible of poor performances in some cases.
One of the most important was that the gain was input-dependant.
We performed multiple experiments, using a step signal, at different voltages.
Ideal current, simulated
Real current, measured
Approximation of f(v)
Least squares
Non Linear Gain

## Slide 29
Identification
As seen from the figure,
f(v)=g(v)/v is a nonlinearity with
sector [a,b], a >0, b < infinity.
Results:

## Slide 30
Identification
Motor Electrical Friction
Minimize a cost function
Or use the fact that the current is WN
Find c?

## Slide 31
Identification
1. Minimize:
=> c= 0.4621, using genetic algorithm
Use an iterative method:
  Find the set where
  Check if the current in that set is WN using the Anderson Whiteness Test
  If not, repeat with
  => C = 0.35

## Slide 32
Identification
Plot of
C=0.46 slightly outperforms C=0.35

## Slide 33
Identification
Static Friction
Another interesting problem was to identify the static friction of the entire system.
How can we do that?
Encoder have resolution of 14 bits => 16384 steps. Then the resolution in cm is
560/16384 = 0.0342 cm.
Use a linearly increasing input voltage, check for which t: ,
Then:
Where N is the load,
i the current at time t.
Force transmitted
Knowledge of the other
Nonlinearities was needed
In order to estimate the friction
Correctly!

## Slide 34
Identification
Static Friction

## Slide 35
Identification
Filtering

## Slide 36
Identification
Noisy current sensor, third encoder not available. How to do state feedback,
Pole placement, etc…?
Use of Luenberger/Kalman observer. Tests done:
Estimate of the carts position (all 3 degree of freedom) using only the current.
Estimate of the carts position (second and third cart) using the current and the data from the first encoder.
Estimate of the carts position (second and third cart) using only the data from the first encoder.
90% fit

## Slide 37
Control
Control

## Slide 38
Loopshaping
Poles coming from the cart dynamics.
We would like to cancel this behavior.
3Hz

## Slide 39
Loopshaping
cancel out cart dynamic
Integral action
causal block

## Slide 40
Loopshaping

## Slide 41
Loopshaping
Transient does not take into account non-linearities,
but rising time and steady-state value match what we expected.

## Slide 42
Positive zeros
What if there is another helpful position for the zeros of the regulator?
Admissible Area wrt Performance
Cart Poles

## Slide 43
Positive zeros

## Slide 44
LQG
computed in order to guarantee zero tracking error at steady-state.
Notes: LQG is a state-feedback controller => Kalman.
How do we weight Q and R?
Why didnt we include an integral action.

## Slide 45
LQG
The compensator is not perfect even though error is below 1/100.

## Slide 46
LQG 2dof

## Slide 47
LQG 3dof

## Slide 49
1Hz
The weights should have the inverse shape of the desired sensitivity.
The higher the weight the weaker the control action:
It is important since the motor saturates at ±5V.

## Slide 51
Reducing the order of complexity of the regulator does not alter perfomance.

## Slide 52
Zero tracking error
Rising time less than 1 sec
Noise cancellation

## Slide 53
2dof
Notes: We feedback from the second output

## Slide 54
2dof

## Slide 55
2dof
The current is not directly measured, but estimated through a Kalman filter.
The current regulator allows to stabilize the motor effort.

## Slide 56
2dof

## Slide 57
3dof

## Slide 58
3dof
The response (although not perfect) is way more stable with the inner current loop.

## Slide 59
EKF
Extended Kalman Filter

## Slide 60
EKF
Linear Model
Nonlinear Model

## Slide 61
EKF
Steps:
Update state estimate
Linearize system around
Update Kalman gain
Update prediction
Notes: Discrete time because it works better.
There is no implementation of EKF on matlab.

## Slide 62
EKF
Simulink simulation
Porting onto Arduino
Validation of results
Notes: Correctness of implementation
Noisy data, Online
Comparing Arduino vs Simulink = Online vs Offline

## Slide 63
EKF

## Slide 64
THANK YOU!
QUESTIONS?