## Slide 1
Control of linear vibrations
Russo Alessio, Savaia Gianluca, Alberto Ficicchia
School of Industrial and Information Engineering
Politecnico di milano
AUTOMATION AND CONTROL LABORATORY
Automation and Control Engineering 2015/2016
https://github.com/rssalessio/linearVibrationsControl

## Slide 2: System descrption Control of linear vibrations
POLITECNICO DI MILANO
System: brushed motor, 3 carts, 3 springs, weights, 4 encoders, PoliArd/Arduino
Preliminary issues:
Arduino saturation limits measured motor current to ±5A
For , is not constant; assumed
Encoder signal: Arduino to and fro cm; measurement of the ratio
Protection system - four macroblocks:
Input Manager: selects input, control input noise and reference
Protector: saturates voltage, displacement and reference; synchronizes Arduino and signal starting time; triggers alert
System: motor and encoder feedback
Controller: controls + pulls control voltage to 0 when alert has been triggered

## Slide 3: Modelling Control of linear vibrations
POLITECNICO DI MILANO
Motor: where
: back-emf effect, : torque constant
Pinion/rack: where
: load torque transmitted to the carts
: inertia of motor, pinion and rack
: non linear motor friction
: total damping (viscous + spring) of the i-th cart
Putting and neglecting nonlinear friction
where
Each cart: where

## Slide 4: 1 DOF Control of linear vibrations
POLITECNICO DI MILANO
: state of the motor (current)
: position of the cart
: position of the cart
: velocity of the cart
2DOF: Lagrangian approach: where
State space model:
With suitable definitions of M, C, K, B
Analogously for 3 dof

## Slide 5: White box identification: detached cart Control of linear vibrations
POLITECNICO DI MILANO
The cart was released from a fixed position and allowed to oscillate:
- ; T : time difference between first and second peak
- , ; : amplitudes of first and second peaks
- : for each spring two experiments, with and without load:
- varies with M (ball bearing friction?):
Validation: real output vs simulation (identified parameters):
fit=0.9449±0.0263
Loss of accuracy on the long run

## Slide 6: White box identification: motor only Control of linear vibrations
POLITECNICO DI MILANO
Resistance only: voltage pulses to motor: steady state measurement of
Resistance and inductance: experimental input/output data given to Matlab tfest (first order)
; back-emf neglected because
,
Nominal values from motor datasheet
,
Validation: real output vs simulation with input = N(0,9/4): fit=0.8142±0.0364

## Slide 7: Overall system identification Control of linear vibrations
POLITECNICO DI MILANO
System mass: ; Motor mass:
System springs: , ,
System damping(load/no load):
, ,
, ,
Linear torque constant:
Validation: real output vs simulation with input: where :
Fit:
1 dof: (85.42±1.68)%
2 dof (2 combinations: Kh-Km, Kl-Kh): (86.54±4.68)%
Same tests and same techniques used for detached parts. Results:

## Slide 8: Overall system identification Control of linear vibrations
POLITECNICO DI MILANO
1 dof Kl
2 dof Kl Kh
2 dof Kh Km
1 dof Kh